## Slide 1: But It’s Not Dead Yet! Early Replacement Measures Phase II Study: Selected Findings and Recommendations
January 21, 2016
Evergreen Economics
PWP Inc.

## Slide 2: Presentation Objectives
Illustrate dual baseline method for early replacement project analysis
Show how accurate data and proper methods are required for accurate cost effectiveness calculations
Give overview of recommended methods and tools for early replacements
  Methods are not difficult to apply!
  Methods already used by various PAs – but inconsistently – are not brand new!
Notes: Note: All of the CT, MA and NH ER programs were using dual baselines when we started the research in 2014.
Other states use dual baselines too – Arizona, Arkansas

## Slide 3: Definitions
Normal Replacements (NR):
  Non-operational equipment at end of its useful life
  Equipment replaced for any other reason without a program intervention
      Functionally obsolete
      Not needed due to occupancy changes
Early Replacements (ER):
  Operational equipment that is replaced prior to typical time of normal replacement – if no program intervention
  Timing of replacement has been moved forward
Notes: Normal Replacement – replacement outside a program for any reason

## Slide 4: ER Savings Analysis
Two equipment lifetimes used with dual baselines:
  Effective useful life (EUL)
  Remaining useful life (RUL)
Notes about RUL:
  Reflects that equipment would have remained in place without an ER program
  During the RUL savings should be based on the existing installed equipment
  Savings after the RUL should be based on a code-compliant baseline
Notes: EUL = the age at which 50% of installed equipment will continue to operate
RUL = difference between current age of equipment and the time of normal replacement, GIVEN THAT THE EQUIPMENT IS IN PLACE AND STILL OPERATING. Later we’ll show how survival curves are used to compute RUL.

## Slide 5: Dual Baseline Illustration
Notes: * Note that horizontal axis is TIME
* The RUL – T2-T1 – and assumed energy efficiency of the future new equipment – B in the diagram – have important impacts on ER measure savings, incremental costs, and cost effectiveness, and can inform measure eligibility and incentive levels.

## Slide 6: Program Design & Participation Also Examined
ER and NR customers phone survey (n=373)
    Old equipment age and characteristics
    Reasons for replacing equipment
    Consideration of repairs v. replacement
    Furnace/AC combination projects
High-volume ER installation contractors (n=8)
    Customer decision making
    Equipment EUL and RUL estimates
    Typical installation costs
    Opinions about PA ER programs
Report includes findings from:
Notes: The rest of our presentation focuses mainly on RUL, energy savings and incremental cost issues, but we also conducted some qualitative research on motivations for ER projects and installation contractor practices.
Findings cut across multiple states – NH, MA, CT, MD
Detailed findings from these activities are in the final report.

## Slide 7: RUL Current Practices
Limited PA tracking of old equipment age (and efficiency)
RUL is not based on observed age of replaced equipment
    Example: RUL = 5 years always
Calculated RULs not consistent with definition of EUL and empirical survival data
    Example: RUL = (EUL for all installs – Age)+

## Slide 8: Recommended RUL Method
Chart: Age (years)
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0 | 41.0 | 42.0 | 43.0 | 44.0 | 45.0 | 46.0 | 47.0 | 48.0 | 49.0 | 50.0
Series 1 | 1 | 0.99931 | 0.99681 | 0.99218 | 0.98525 | 0.97591 | 0.96413 | 0.94988 | 0.93319 | 0.91412 | 0.89277 | 0.86925 | 0.8437 | 0.8163 | 0.78723 | 0.75669 | 0.72491 | 0.69211 | 0.65853 | 0.62439 | 0.58995 | 0.55542 | 0.52103 | 0.48699 | 0.45351 | 0.42077 | 0.38893 | 0.35815 | 0.32855 | 0.30025 | 0.27332 | 0.24784 | 0.22386 | 0.2014 | 0.18048 | 0.16108 | 0.14319 | 0.12678 | 0.11178 | 0.098162 | 0.085845 | 0.074763 | 0.064841 | 0.056001 | 0.048162 | 0.041246 | 0.035173 | 0.029867 | 0.025252 | 0.021258 | 0.017819
Series 2 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723 | 0.78723
Series 3 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361 | 0.39361
Median Residual Life (MRL) – 14 yr. old furnace
Notes: This method uses an estimated survival function that determines the probability distribution of the age at replacement of a specific type of equipment.
Arkansas, Texas and Louisiana use survival curves for RUL.
Reflects fact that the probability that equipment will reach a given age increases with current age.
In this example, the EUL for all furnaces is 22.6 years (LBNL estimate)
Just using the furnace age of 14 years and this EUL would result in an RUL of 8.6 years
At age 14 years, however, the median replacement age for surviving equipment increases to 25.9 years, for a median residual life of 11.9 years.
This is the method we used to calculate RULs

## Slide 9: RUL Method Matters!
Chart: Age at Replacement
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0 | 41.0 | 42.0 | 43.0 | 44.0 | 45.0 | 46.0 | 47.0 | 48.0 | 49.0 | 50.0
Median Res Life | 22.6163 | 21.6264 | 20.6632 | 19.7314 | 18.8336 | 17.9715 | 17.1461 | 16.3579 | 15.607 | 14.8931 | 14.2156 | 13.5738 | 12.9666 | 12.3928 | 11.851 | 11.3399 | 10.8579 | 10.4036 | 9.9755 | 9.572 | 9.1918 | 8.8334 | 8.4955 | 8.1767 | 7.8758 | 7.5918 | 7.3235 | 7.0698 | 6.8298 | 6.6026 | 6.3873 | 6.1833 | 5.9897 | 5.8059 | 5.6312 | 5.4652 | 5.3071 | 5.1566 | 5.0131 | 4.8762 | 4.7456 | 4.6208 | 4.5016 | 4.3875 | 4.2783 | 4.1736 | 4.0734 | 3.9772 | 3.8849 | 3.7962 | 3.7111
Deemed RUL | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5
EUL - Age | 22.6163 | 21.6163 | 20.6163 | 19.6163 | 18.6163 | 17.6163 | 16.6163 | 15.6163 | 14.6163 | 13.6163 | 12.6163 | 11.6163 | 10.6163 | 9.6163 | 8.6163 | 7.6163 | 6.6163 | 5.6163 | 4.6163 | 3.6163 | 2.6163 | 1.6163 | 0.61627 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Average RUL | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9
RUL Comparison - Furnaces
Notes: This slide shows the consequences of using different RUL calculation methods. You will get different values depending on age of equipment and method used.
Average RUL in Red was calculated by Evergreen using Residual Median Life Method for each individual project.
Shows that for furnaces we derived RUL values higher than the deemed values used by some PAs

## Slide 10: RUL Findings
A | B | C | D | E | F
ER Measure | Projects with Age Data | Range of Reported Ages | Range of Computed RULs | Average of Computed RULs | PA Deemed RULs
Furnace | 214 | 8-61 | 3-16 | 8-9 | 5/6
Boiler | 108 | 9-98 | 3-16 | 6-9 | 5/10
CAC | 52 | 10-28 | 5-10 | 7 | 5
Variation in Equipment Age and RULs
Deemed RULs are not consistent with estimates from recorded project ages
Notes: Findings on this slide based on PA age data provided to us.
Not all projects had complete data –e.g., replaced equipment age and/or efficiency. Data issues noted in report.
We used EULs and survival curves from LBNL Report and DOE to calculate Median Residual Life
KEY FINDING = Wide range of replaced equipment ages
KEY FINDING = RUL is not 0, even for oldest equipment
KEY FINDING = PA RUL values are generally lower than what we computed
KEY FINDING = Possible that PAs are leaving savings on the table, and/or paying too much for some projects with high RUL

## Slide 11: ER Furnace –Age & Efficiency
Most furnaces replaced in the ER programs were less than 30 years old
Most furnaces replaced in the ER programs were reported to have an efficiency rating of 80%

## Slide 12: ER Boilers –Age & Efficiency
Most boilers replaced in the ER programs were 20 to 30 years old
Most boilers replaced in the ER programs were reported to have a 78% to 82% efficiency rating

## Slide 13: ER AC – Distribution of Ages
All ACs replaced in the ER programs were less than 30 years old
Efficiency of replaced ACs was not reported

## Slide 14: Energy Savings Current Practice
Dual Baseline:
  Years < RUL: Baseline = Replaced Efficiency
  Years > RUL: Baseline = New Standard Efficiency
Replaced Efficiency:
  Often deemed
  Sometimes site-specific
Standard Efficiency:
  Typically assumes no change in current standard
Notes: Note: All of the CT, MA and NH ER programs were using dual baselines when we started the research in 2014.

## Slide 15: Baselines Will Change…
Equipment | Expected Update | Potential Effective Date | Proposed Standard
Furnace | 2016 | 2021 | 92 AFUE
Gas Boiler | 2016 | 2021 | 85 AFUE
Central AC/Heat Pumps | 2017 | 2022 | TBD
Future DOE Standards:
Notes: Gas furnace baseline efficiency increased to 80% in 2015. Next changes in 2021.
Gas boiler baseline now 82%. Next changes in 2021.
Next changes to CAC and Heat Pumps in 2022.
DOE codes on 6 year cycle
No locations in NEEP territory exceed federal standards for residential HVAC.

## Slide 16: ER Incremental Cost (IC) Calcs
Some existing methods overstate or understate IC:
    Overstated when IC = New EE Measure Cost
    Understated when IC = New EE Measure Cost – Discounted Standard Equipment Cost
ER shifts the entire future cycle of normal replacements for a piece of equipment
IC = New EE Measure Cost – Standard Equipment Cost + (ER Cost Factor * Standard Equipment Cost)
    Formulas for ER Cost Factor are in report
    Formulas use RUL value
    Not difficult to calculate
Notes: The ER Cost Factor represents the cost, in percentage terms, of bringing forward to the present the future “normal” replacement of the existing equipment.
Getting RUL right matters for cost-effectiveness

## Slide 17: ER Incremental Cost – Example
Key Point: Incremental cost of ER increases with RUL
This example shows how the ER Cost Factor is used to compute the IC of an ER high-efficiency furnace
Notes: MORE KEY POINTS:
A 40 yr old furnace is less costly to replace and may still be producing savings – program should not automatically disqualify the oldest equipment.
Projects with high RUL may produce savings over a longer timeframe, but also have higher IC – these move in the same direction.

## Slide 18: ER Cost-Effectiveness (CE)
Impacts of RUL on Cost Effectiveness:
  Lower RUL => Lower efficiency of old equipment
  Lower RUL => Lower current standard efficiency
  Lower RUL => Higher annual energy savings
  Lower RUL => Lower incremental cost

## Slide 19: RUL Recommendations
Track age and efficiency of old equipment during program implementation
Calculate site-specific RUL as a function of age and survival function
    i.e., Median Residual Life method
Ensures consistency of EUL and RUL
    EUL = median value of a survival function
    EUL = the age at which 50% of equipment will continue to operate
Second best = use deemed RUL value from a current study sample
Notes: It is more difficult to assemble age, efficiency data after the program has ended. Do it during implementation.

## Slide 20: Savings and Costs Recommendations
Calculate savings using site-specific RUL and efficiency
Review consistency of code-compliant baseline and RUL assumptions
Revise baseline if efficiency standard is projected to change during RUL for many participants
Use the ER Cost Factor to calculate project level incremental costs

## Slide 21: Program Design Recommendations
Maximum repair cost (e.g., $1000) may be reasonable qualifying criterion
Maximum replaced efficiency may be advisable to ensure savings
Don’t use maximum age criteria - older units may be the most cost-effective to replace
Age is not a basis to discriminate ER/NR
ER Incentive Eligibility:
Notes: We found that most households won’t spend more than $1,000 on repairs – the equipment has essentially failed.

## Slide 22: Program Design Recommendations
Incremental cost can be used to benchmark ER incentives
Besides age and efficiency, PAs may want to collect other data during installations that may be useful in program evaluation, but which are difficult to obtain at a later date:
    Functional status of replaced unit
    Repair costs
    Other factors influencing decision to replace
Other ER Design Elements:

## Slide 23: Multiple Resources for Equipment Age and Efficiency
Manufacturer websites have model/serial lookups
Other websites:
  http://www.buildingcenter.org/content/hvac-production-dateage
  www.inspectorsjournal.com/forum
  www.nachi.org/forum
Equipment maintenance tags (for min. age)
ENERGY STAR efficiency estimates by age of home
Energy efficiency degradation factors:
  National Renewable Energy Laboratory’s “Building America House Simulation Protocols”
  Used in AR TRM
Notes: Other equipment information sources are listed in the report appendices

## Slide 24: Resources and Tools
Equipment survival curves from LBNL and DOE:
Etc….
Notes: Survival curve tables and formulas included in our report appendices

## Slide 25: Key Takeaways
PAs are already using these methods in some form:
    Dual baselines
    Survival curves
    ER Cost Factor (i.e., deferred replacement credit in MA)
These are not new approaches
Using site-specific data avoids estimating blended EUL/RUL lifetimes, doing inaccurate cost calculations

## Slide 26: Questions?

## Slide 27: For Additional Information
  Elizabeth Titus
  etitus@neep.org
  (781) 860-9177 ext. 111
  Stephen Waite
  spwaite3@comcast.net